## Slide 1
IROS 2022 Workshop on Assistive Robotic Systems for Human Balancing and Walking: Emerging trends and perspective
Equilivest: A Robotic Vest to aid in Post-Stroke Dynamic Balance Rehabilitation
Paviotti Franco1, Buniak Esteban1, Ramele Rodrigo1, Orestes Freire2, Santos Juan Miguel3
October 27th, 2022
1 Instituto Tecnológico de Buenos Aires (ITBA), Buenos Aires, Argentina
3 Universidad Nacional de Hurlingham, Buenos Aires, Argentina
2 Centro de Integral de Neurorehabilitación, Buenos Aires, Argentina

## Slide 2
Caplan 2022 [1], Donato 2016 [2]
Cerebrovascular disease / Stroke
Main cause of disabilities worldwide [1]
After first six months of treatment most patients reach a steady state with slow improvements.
Patients who recover ability to walk
Falling or sudden balance lost is one of stroke’s most common secondary effects, impairing autonomy, independence, Activities of Daily Living (ADL).
Causes: dysmetria, feet sensation loss, proprioception issues, ataxic gait, bradykinesia, affected vestibular processing among many other reasons, every case being a unique situation.
Introduction
1/10

## Slide 3
36 years-old, healthy, female patient.
Acute brainstem stroke on posterior fossa subarachnoid after giving birth due to a brain artereovenous malformation (AVM) [3]
After 1-Month in induced coma, unable to walk, move, talk or swallow.
Throughout a first period of intensive rehabilitation, managed to recover significantly.
Discharged from hospital, 7 months after event.
Patient Case Study
Boseman 2015 [3]
Remaining affection is related to dynamic balance problems while walking.
  Satisfactory index scores in static balance tests. Successful hip-balance, ankle-balance tests.
  Recovered lower limbs strength.
  Increase Risk of Falling: Walking on open spaces, confronting lights, concentration fades. Non-lateralized.
  Able to walk with Canadian canes and under constant supervision
  Current Treatment: Rehabilitation to retrain Vestibulo-Ocular Reflex (VOR).
2/10

## Slide 4
Human Dynamic Balance System
Donato 2016 [2]
3/10

## Slide 5
Hypothetical Causes and Project Goals
Project Goals
Vestibular
Bradykinesia
Ataxic Gait
Artificial
Vestibular
Feedback
Falling Risk
Awareness
System
Gait
Pacemaker
  Wearable Actuated Vest: WDBR [3]
  Testbed: iteratively improvements and testing.
  VF: vibro-tactile feedback stimulation
  Motor Control Learning: Assist-as-needed and adaptive VF signal [5]
Peake 2018 [4], Balasubramanian 2010 [5]
4/10

## Slide 6
Equilivest
5/10

## Slide 7
Experiments
Vestibular Information Integration: Participants are told to lean forward performing ankle forward until they can’t maintain balance anymore Goal: Determine breaking point before falls.
Ataxic Gait: Ten-Meter Walking (10MWT) assessment Goal: Identify gait cycle for the pacemaker and gait abnormalities.
Bradykinesia: Combination of previous two experiments Goal: Obtain data of a time series to implement a forecasting procedure, calibrated to the patient.
Experiments
Chart: Time
6/10

## Slide 8
Results
Chart: Angular Acceleration
Chart: roll
7/10

## Slide 9
Presentar mas resultados
Results
8/10

## Slide 10
Conclusions and Future Work
Patient Vest trials will begin next month concurrently acquiring location information from a Motion Capture system.
We will locate an addition IMU on a headset device.
Provide visual feedback based on cameras.
Relative inexpensive IMU sensors are enough to identify fall situations and to derive gain cycle.
Predicting before happening a fall is a much challenging problem.
Basic VF can be provided from the information obtained from IMU sensors.
Neurorehabilitation tools are alternatives not procedures, that could be useful when other traditional options are not present.
Work in progress
9/10

## Slide 11
Thank you and Q&A
IROS 2022 Workshop on Assistive Robotic Systems for Human Balancing and Walking
Emerging trends and perspective
10/10

## Slide 12
10/10
[1] L.R.Caplan,R.P.Simon,andS.Hassani,“Chapter27-cerebrovascular disease—stroke,” in Neurobiology of Brain Disorders (Second Edition), M. J. Zigmond, C. A. Wiley, and M.-F. Chesselet, Eds. Academic Press, 2023, pp. 457–476. [2] S. M. Donato, K. H. Pulaski, and G. Gillen, “Chapter 19 - overview of balance impairments: Functional implications,” [22] in Stroke Rehabilitation (Fourth Edition), fourth edition ed., G. Gillen, Ed. Mosby, 2016, pp. 394–415.
[3] Boseman, T., Orman, G., Boltshauser, E., Tekes, A., Huisman, T. A. G. M., & Poretti, A. (2015). Congenital abnormalities of the posterior fossa. Radiographics, 35(1), 200–220. https://doi.org/10.1148/rg.351140038
[4] J. M. Peake, G. Kerr, and J. P. Sullivan, “A critical review of consumer wearables, mobile applications, and equipment for providing biofeedback, monitoring stress, and sleep in physically active populations,” Frontiers in physiology, vol. 9, p. 743, 2018.
[5] S.Balasubramanian,H.Zhang,S.Buchanan,H.Austin,R.Herman,and J. He, “Cooperative and active assistance based interactive therapy,” in IEEE/ICME International Conference on Complex Medical Engineering. IEEE, 2010, pp. 311–315.
References